## Slide 1
Mobile Robotics Hackathon 2026 · TU Dresden
LandMate
A mobile landing pad for drones
"We built a ground robot that watches the sky, predicts where a drone will land, and drives there before it hits the floor."
Clutch Robotics
1 / 7

## Slide 2
Drones fall.
Nobody is ready.
Saturday 11:00 — WHERE WE STARTED
An ANT1 ground robot that drives on command. A Crazyfile drone that hovers. Zero connection between them. When the drone descends → nobody knows where it will land.
→
Sunday 17:00 — THE QUESTION WE ASKED
Can a ground robot... SEE the drone from below, PREDICT its landing point in real time, INTERCEPT it before it hits the floor?
2 / 7

## Slide 3
Approach
3 / 7

## Slide 4
How LandMate catches a drone
4 / 7

## Slide 5
What runs right now
8 / 10
interception success — 5 sim scenarios
<300ms
detect-to-predict latency per frame
5 / 7
Notes: → Detects the drone in a sky-facing camera frame
→ Estimates altitude and velocity from a single camera (no depth sensor needed)
→ Predicts where the drone will land and in how many seconds
→ Drives to the intercept point — stops when the 60×40 cm pad is centred under the drone
→ Aborts if the ANT can't reach the spot in time (reachability gate)

## Slide 6
Our biggest challenge and next step
The hard part
1
The challenge
Varying drone positions.
2
First attempt
We removed unreliable detections, but the estimated position still jumped.
3
What improved it
A Kalman filter smoothed the motion estimate, making the predicted landing point more stable.
4
What we learned
Reliable landing predictions need stable tracking first.
Next step
Scaling to handle multiple drones and coordination between multiple ground robots.
6 / 7

## Slide 7
Thanks, from ClutchRobotics!!!
7 / 7

## Slide 8
Appendix: Video Demo

## Slide 9
Appendix: Architecture

## Slide 10
Appendix: Architecture